MAGPIE Probes – Science, Methods, and Site-Specific Goals
MAGPIE Probe Network: Science & How We Measure It
6 identical probes, pole-to-pole coverage
Time-synchronous meteorology + electrification + imaging
Descent profiles + landed stations → vertical + horizontal context

---
Instrument Suite
- Meteorology
  - Pressure (±0.5 Pa), Temperature (±0.1 K), Humidity (±2 %RH), CO₂ (ppm)
  - Solid-state thermal anemometer (±40 m/s, 10–50 Hz fast response)
- Electrification
  - Broadband E-field antenna + low-noise preamp (DC–100 kHz equivalent paths)
- Acoustics
  - Microphone 20 Hz–12 kHz (wind, dust impacts, microquakes, mech. events)

---
Instrument Suit (Cont)
- Navigation & Descent Profiling
  - 9-axis IMU (200 Hz), altimeter (tbd on radar) (up to 20 Hz), tri-axis magnetometer
- Cameras
  - Side still camera (color): horizon-looking, single-frame or burst, nearby rock, regolith and startracking
  - Bottom-facing descent camera (color): nadir imagery during EDL
  - Side thermal camera (low-res, equal view with side still): scene temperature contrast (frost, cloud edges, dust fronts)
- Power & Comms
  - Li-ion (86 Wh) + solar trickle; survival Li-FeS₂ (18 Wh) at poles
  - UHF 433 MHz (3 W) + LoRa 915 MHz (1 W) with adaptive data rate

---
Measurement Method & Cadence
- During Descent (EI → chute → retro):
  - IMU @ 200 Hz; radar altimeter @ 10–20 Hz → vertical density/temperature via dynamic pressure + profile inversion.
  - Bottom camera: 1–5 fps burst near key events (chute inflate, backshell sep, pre-flare). Ground-texture scaling for optical flow wind estimates near surface.
  - Side color: 1–2 frames pre-parachute and post-deploy for cloud bands/dust sheets against the horizon.
  - Thermal (side): 1–2 fps snapshots of scene temperature contrast (frost lines, cloud opacity gradients, warm dust plumes).
- On the Surface (14-sol nominal):
  - Met core (P/T/RH/CO₂): 1 Hz burst for 5 min every 15 min; 0.1 Hz background.
  - Wind (thermal anemometer): 10–50 Hz bursts (gust capture), 1 Hz background.
  - E-field: continuous low-rate monitor + 2 s high-rate events on threshold.
  - Acoustic: 10 s clips each 5 min; event-triggered (dust impacts/microquakes).
  - Side color still: 1–3 images per sol timed for morning/afternoon; storm triggers add bursts (up to 5 extra frames).
  - Thermal (side): paired with every color still + 2–3 extra frames at local night/morning for frost detection.

---
Calibration & Quality
- P/T/RH zero/offset via pre-flight chamber curves + in-situ cross-checks (nighttime stability).
- E-field quiet-state baseline nightly; microphone self-noise sweep hourly.
- Camera radiometry via internal flat and sun-angle geometry; thermal NUC & two-point ref (radiator + sky).

---
Data Products
- Time series: P, T, RH, CO₂, wind vectors, E-field, acoustic spectra
- Descent profiles: density/temperature vs altitude; wind shear estimates
- Imaging: side color/thermal pairs (radiance & apparent temperature maps), bottom camera descent mosaic (landing context, grain size proxy)
- Events: dust devils (pressure dips + E-field spikes + acoustic hiss), gust fronts, frost growth/retreat, chute inflation dynamics
- Derived maps: local roughness/albedo (bottom cam), cloud opacity edges (side color/thermal), near-surface lapse rate

---
Site-Specific Goals

---
Olympus Mons Flank (High Altitude / Orographic)
- Goals
  - Quantify up-down-slope flow, wave activity, and cloud microclimates.
  - Assess turbulence/hazard models for future aerial assets. Including sister probes
- How we measure
  - Anemometer: gust & wave packets (10–50 Hz bursts at slope-wind peaks).
  - P/T/RH/CO₂: diurnal mountain-circulation signatures; nocturnal inversions.
  - Side color + thermal (paired): orographic cloud edges; thermal contrast to infer cloud optical thickness/dust entrainment.
  - Bottom cam (descent): surface roughness & flow-aligned streaks leads to wind orientation validation.
- Data products
  - Turbulence intensity spectra, cloud edge motion vectors, slope-wind climatology.

---
Hellas Planitia (Deep Basin / Human Landing Candidate)
- Goals
  - Characterize dense boundary layer, dust loading, storm amplification.
  - Evaluate human EDL benefits, resource (ice) likelihood, potential lava-tube skylights.
- How we measure
  - Pressure: enhanced tides & storm surges (high-amplitude);
  - E-field + acoustic: dust-devil electrification; saltation impacts.
  - Side color + thermal (paired): dust wall opacity and thermal contrast, frost patches in mornings.
  - Bottom cam (descent): albedo/texture leads to determining regolith grain size proxy; skylight/pit detection cues.
  - Wind: gust fronts at basin edges; shear near storm passages.
- Data products
  - Electrified dust-storm catalog; landing-hazard map (texture/rockiness), frost occurrence vs pressure cycles; candidate skylight snapshots.

---
Planum Boreum (North Polar, late summer)
- Goals
  - Track CO₂ frost sublimation and volatile export; polar vortex near surface.
- How we measure
  - Thermal (side) at dawn/dusk: frost/ground temperature contrast leads to observation of sublimation.
  - P/T/RH: vapor gradients; CO₂ sensor for local enrichment.
  - Wind: katabatic flows off cap edge.
  - Side color: seasonal albedo changes; cloud bands.
  - Acoustic: low-freq microtremors from thermal cracking/wind-driven grains.
- Data products
  - Frost retreat rate (m/day), near-surface lapse rates, katabatic climatology.

---
Planum Australe (South Polar, seasonal accumulation)
- Goals
  - Hemispheric comparison of volatile cycle; CO₂ deposition and circulation.
- How we measure
  - Same toolkit as Boreum, flipped seasonality: more frequent thermal+color pairs during accumulation; night thermal snapshots.
  - Radar altimeter + IMU (descent) improve density model in cold cap air.
- Data products
  - Deposition events log, frost growth curves, south-pole boundary-layer structure.

---
Equatorial Site A (Volcanic Plains / Solar-Rich)
- Goals
  - Diurnal convective cycles, dust-devil climatology, lava-tube context.
- How we measure
  - P/T/RH: strong daytime superadiabatic layers;
  - Wind: convective gusts; devil cores via rapid pressure dips.
  - E-field + acoustic: devil charge and grain impacts;
  - Side color + thermal: moving dust fronts, heated surfaces;
  - Bottom cam (descent): flow streaks, polygonal cracking leads to determing roughness & hazards.
- Data products
  - Dust-devil occurrence map (per sol), convective boundary-layer growth curves, thermal inertia proxies.

---
Equatorial Site B (Flexible/Target of Opportunity)
- Goals
  - Fill science gaps, chase active weather corridors, or sample hydrated mineral/ancient valley terrain for astrobiology relevance.
- How we measure
  - Adaptive cadence rules: boost side color/thermal pairs during storm season; add extra acoustic clips during high winds; image sequences for valley haze.
- Data products
  - Adaptive cadence rules: boost side color/thermal pairs during storm season; add extra acoustic clips during high winds; image sequences for valley haze.

---
Trigger Logic & Event Modes
- Dust event trigger: pressure dip + E-field rise leads to high-rate wind, acoustic, image burst (side color + thermal).
- Frost trigger: pre-dawn thermal contrast > threshold leads to adding thermal frames + RH bursts.
- Gust trigger: wind variance spike leads to raise anemometer rate & mic clips.
- Comm window packing: prioritize compressed bursts, then baseline met.

---
From Raw to Insight
- Descent inversion: IMU + radar alt leads to density/T profile; wind shear from optical flow (bottom cam).
- Surface fusion: P/T/RH + wind + E-field + acoustics leads to event classification (devil, gust front, front passage).
- Imaging fusion: side color & thermal co-registration leads to cloud opacity & dust thermal contrast.
- Products shipped per pass: daily summary + event packets (~1.5 MB per pass).

---
Why This Matters (for humans & climate)
- First synchronous, multi-latitude boundary-layer dataset leads to better forecasting.
- Scalability of mission and mission hardware.
- Landing site safety: turbulence, visibility, ground roughness, dust load.
- Resources: frost/ice mapping, hydrated terrain cues, potential skylight imagery.
- Validates climate & EDL models; de-risks human missions.